## Slide 1: Recent Trends in VLSI Design, Signal Processing & Optimization based on EDA tools
Date 10/11/2020 Time 10am onwoards

## Slide 2: Hardware implementation of Multirate DSP blocks
1] Downsample Block downsample(x,n)
2] Upsample Block upsample(x,n)
3] Decimation Block decimate(x,n) [ filter + downsample ]
4] Interpolation Block interp(x,n) [ upsample + filter ]

## Slide 3
Downsample effect on signal

## Slide 4
upsample effect on signal

## Slide 5
decimate effect on signal

## Slide 6
interpolation effect on signal

## Slide 7
Application:- Simple Channelizer using up and down sampler
Let there are 4 signals and need to transmitted these signals using a single channel
1] Signals are x1, x2 ,x3 x4
2] upsample these signals by 4
3] pads 0s to x2 to x4 by 1, 2, 3
4] add all to create the mix signal
5] transmitted it
6] downsample it by 4 , thro chain of delay block with value 0 1 2 3
7] you will get the all 4 signals back ,

## Slide 8: Advantages / Applications
Data converters
High resolution display
Reduces the storage requirement / memory
oversampling
reduced order filters
lower sampling rate
realizable filters
faster and easier calculations
interpolating the data
discard undesired samples
pack-unpack => zip/unzip
and many more

## Slide 9: For hardware implementation Tools required are as
Matlab:- for signal generation and design code for multi-rate units
Active HDL:- for hdl code design, compile and simulate
Vivado :- Hardware platform for syntheses and validation by simulation

## Slide 10
Basic elements needed for implementation of multirate units are as
1] D flip-flops
2] mux
3] clock divider
4] clock multiplier , PLL / MMCM IP can be used for this
5] filter , here we are using 19-20 tap fir filter
6] for clock controlling fsm may be required
For testing we need signal as well , will generate from matlab

## Slide 11
%% signal generation and convert to 32 bit hex format
clc ; clear all
%%
fs = 6e3; % sampling frequency
t = (0:1/fs:0.2)';
fc = 200; % signal frequency
x1 = 10*sin(2*pi*fc*t)'; % signal
%%
t=[]; % all sample values in variable t (hex 32 bit)
for pnt=1:size(x1,2)
t1 = [ float2bin(x1(pnt)) ];
t = [t;t1];
end
allcnvfiles.txt

## Slide 12
`timescale 1ns / 1ps
module test_signal2();
reg clk,reset;
reg [31:0] datax;
//dut instantiation
initial clk = 1'b1;
always #5 clk = ~clk;
initial begin
reset = 1'b1;
#20 reset = 1'b0;
end
integer file_read,read;
initial
begin
file_read = $fopen("allcnvfiles.txt","r");
End
initial
begin
while (!$feof(file_read))
begin
@(posedge clk);
read <= $fscanf(file_read,"%x\n",datax);
end
@(posedge clk);
$fclose(file_read);
end
endmodule

## Slide 13
entity datagen3 is
port ( clk : in std_logic;
rst : in std_logic;
x : out std_logic_vector(31 downto 0)
);
end datagen3;
architecture Behavioral of datagen3 is
constant N: integer := 1201; --
type arr is array (1 to N) of std_logic_vector(31 downto 0);
constant sd : arr :=
(
x"00000000",
x"40051040",
x"408227de",
x"2a51b191“ );
begin
-- code start
input: process (clk, rst)
variable i : integer := 1; -- i = 0 ;
begin
  if (rst = '1') then
  x <= (others => '0');
  i := 1;
  elsif (clk'event and clk = '1') AND (i<N) then
  x <= sd(i);
  i := i +1;
  end if;
end process;
end ;

## Slide 14
Clock divider

## Slide 15
Clock multiplier >> MMCM/PLL ip
Cover code
IP
TB
Clk out , lockout
Clk in , reset

## Slide 17
Cover code

## Slide 18
test bench code

## Slide 19: Direct form of FIR filter

## Slide 22
Downsampler block diagram
x = [ 1 5 4 6 7 8 9 1 11 4 6 9];
dnx = downsample(x,3);
dnx = 1 6 9 4

## Slide 23: Matlab plot of same data and approach

## Slide 24: Down sampler circuit

## Slide 25: Down sampler circuit simulation result

## Slide 26: Down sampler schematic from vivado

## Slide 27: Down sampler simulation from vivado

## Slide 28: Upsampler block diagram
x = [ 1 5 4 6 7 8 9 1 11 4 6 9];
upx = upsample(x,3);
1 0 0 5 0 0 4 0 0 6 0 0 7 0 0 8….
A B B A B B A B B A B B A B B A….

## Slide 29: Upsampler circuit

## Slide 30: Upsampler circuit simulation result

## Slide 31: Matlab plot of same data and approach

## Slide 32: Upsampler schematic from vivado

## Slide 33: Upsampler simulation from vivado

## Slide 34
Multirate Noble Identities

## Slide 36: Decimation

## Slide 37
Anti-aliasing filter operating at the sampling rate = 6000 Hz
Passband frequency range = 0–800 Hz
Stopband frequency range = 1–3 kHz
Passband ripple = 0.02 dB
Stopband attenuation = 50 dB
Filter type = FIR.
The Hamming window is selected,
since it provides 0.019 dB ripple and 53 dB stopband attenuation. The normalized transition band is given by
Δf = (f stop – f pass )/f s
= (1000 – 800)/6000
= 0.033.
The length of the filter and the cutoff frequency can be determined by
N = 3.3/Δf
= 3.3/0.033
= 100
We choose the odd number, that is, N = 101, and
f c = (f pass + f stop )/2
= (800 + 1000)/2
= 900 Hz.
calculation of filter length and its edge

## Slide 38
x1
d1
y1

## Slide 39
filter

## Slide 43: Interpolation

## Slide 44
Interpolation filter operating at the sampling rate = 18,000 Hz
Passband frequency range = 0–800 Hz
Stopband frequency range = 3–9 kHz
Passband ripple = 0.02 dB
Stopband attenuation = 50 dB
Filter type = FIR.
The normalized transition band is
Δf = (f stop – f pass )/f sL
= (3000 – 800)/18000
= 0.1222.
The length of the filter and the cutoff frequency can be determined by
N = 3.3/Δf
= 3.3/0.1222
= 27,
and the cutoff frequency is given by
f c = (f pass + f stop )/2
= (3000 + 800)/2
= 1900 Hz.
calculation of filter length and its edge

## Slide 45
x1
u1
y1

## Slide 46
filter

## Slide 54
Thank you
Any questions

## Slide 55: Content will be discussed as below
Natural flow of code to chip design
Code >> RTL >> schematic and layout
Details of code is not important here ,
Only functionality we will take into account
I will try my best to make you closer to vlsi-dsp concepts and practical approach if you are ready there.

## Slide 56
Critical path [ longest path without ff ]
Or longest path of combinational circuit
Basic terms that I will use here [expecting all you know these terms]

## Slide 58: From where Signals we will use [matlab]
Expecting some background of matlab
we are taking matlab help for all conversions
Float <> fixed <> hex <> decimal etc
Coefficient conversion etc
and primary design idea like filter design etc.
Filter design for number of taps that we are going to see in rtl design
Signal generations as test signal for circuit

## Slide 59: How we will go for vlsi-dsp design here ?
Will create a
Hdl code
first
Will test the
Code
[simulation]
Signals gen from
matlab
Xilinx
For
Fpga imp
Cadence
Synopsys
tools
rtl ,
area
power
Chip layout
and other important info.
For prototype testing

## Slide 60
Sys_setup
command
Folder with
Code
files
>> codes .v / .vhd
>> 45nm synopsys script file [give RTL]
>> 90nm synopsys script file [give RTL]
>> encounter script file [chip layout]
>> icc script file [chip layout]
>> nclaunch for compile and simulation
>> prime time script file
>> output result goes into this
>> rc compiler script file [give RTL]
>> temp [not in use]
>> work from this we run the tools
Design vision tool gives >> rtl , area , power and other important info.
Encounter , ICC compiler gives >> chip layout and other information.
Rtl compiler gives >> rtl , area , power and other information.
Nclaunch/vcs >> simulation ,hdl to c model from verification [vcs]
To run the tcl file command is >>> Source filename.tcl <<<
Code file and tool setup

## Slide 61
Every script file has these main steps
Read .v / .vhd codes
Analyze the codes
Elaborate the main top module
And rest of the things are
lib path ,
report files generation etc.

## Slide 62
direct_form_of_fir_filter1_coeff1_setup1
direct_form_of_fir_filter1_csymt1_setup1
transpose_form_of_fir_filter1_setup1
test_df_filter14
test_tf_filter141
test_tf_filter142 (coeff sys)
AHB_Testsys
AXI
Fix_add_mul_test1
Fp_add_mul_test1 >> for tool flow walkthrough
http://spiral.ece.cmu.edu/mcm/gen.html
https://www.h-schmidt.net/FloatConverter/IEEE754.html
https://www.micro-ip.com/product.php?cid=428
http://ngspice.sourceforge.net/spices.html

## Slide 63: Current Trends in VLSI Design
1] Smaller device's, increasing the wafer dimensions
2] High speed
3] Low power
4] bicmos , soi , etc
5] asic, soc,
6] High density FPGA’s
8] Memories
9] High frequency RF communications
10] High speed low power processor, single core, multi-core
11] High speed data convertors
12] Communication protocols [ambha, axi, axi4 etc]
13] Compression
14] Cryptography algorithms
15] Image, video processing
16] Interconnect interface [ noc, switch, hub etc]

## Slide 64: Some of the DSP trends and applications

## Slide 65: Understanding AMBA Bus Architecture and Protocols
Advanced Micro controller Bus Architecture (AMBA)

## Slide 66: AHB-Lite block diagram

## Slide 67: Evolution of protocols along with the SOC design trends in industry

## Slide 68: Diagram shows how an AXI interconnect can be used to build an SOC with various functional blocks talking through a master-slave protocol

## Slide 69: AXI Interconnect Core Use Models
Pass Through
Conversion Only
N-to-1 Interconnect
1-to-N Interconnect
N-to-M Interconnect (Sparse Crossbar)
N-to-M Interconnect (Shared Access Mode)

## Slide 72: The interconnect could be a custom crossbar or a switch design or even an off the shelve NOC (Network on Chip) IP that supports multiple AXI masters and slaves

## Slide 73: Pin out of AXI unit , looks complex

## Slide 74: AXI stream waveform
The AXI4 Stream I/F has a high grade of flexibility, it has some signals that are required and many that are optional. The following signals of the bus will be implemented in code: Clock (the AXI stream bus is synchronous)
Data
Ready and Valid (for data flow control)
Tlast (end of packet)

## Slide 75: AXI master stream signalling

## Slide 76: AXI master - slave stream signalling

## Slide 77
APB : The Advanced Peripheral Bus (APB) is used for connecting low bandwidth. peripherals
AHB: The Advanced High-performance Bus (AHB) is used for connecting components that need higher bandwidth on a shared bus.
AHB-lite protocol is a simplified version of AHB. The simplification comes with support for only a single master design.
AXI: The Advanced Extensible interface (AXI) is useful for high bandwidth and low latency interconnects.[AXI-lite AXI-stream.
ACE — AXI Coherence extension protocol is an extension to AXI 4 protocol and evolved in the era of multiple CPU cores with coherent caches getting integrated on a single chip.
ACE-Lite — The ACE also has a simplified version of protocol ACE.
CHI — Coherent Hub Interface — The ACE protocol was developed as an extension to AXI to support coherent interconnects.

## Slide 78: Fixed and floating point
Variable size
32/64 bit size
% A matlab [2018b] code for my way of conversion
% construct struc for fixed
struct.mode = 'fixed';
struct.roundmode = 'ceil';
struct.overflowmode = 'saturate';
struct.format = [32 28];
q = quantizer(struct);
%-------------------------------------------------
v1 = 0.25
v2 = -0.35
d1 = dec2hex(bin2dec(num2bin(q,v1)),8)
d2 = dec2hex(bin2dec(num2bin(q,v2)),8)
d11 = bin2num(q,dec2bin(hex2dec(d1)))
d22 = bin2num(q,dec2bin(hex2dec(d2)))
[num2str(v1) num2str(v2) ,' ' ,d1 ,' ' ,d2, ' ', num2str(d11) ,' ' num2str(d22)]
ans = '0.25 -0.35 04000000 FA666667 0.25 -0.35'

## Slide 79: Schematic of float add mul and LUT no 1602 on kintex7

## Slide 80: Floating point add mul Simulation result

## Slide 81: Schematic Fixed point[32,28] and LUT No 75 on kintex-7

## Slide 82: Fixed point add mul Simulation result

## Slide 86
Synopsys Design Compiler basic tool flow

## Slide 87: RTL level (Register Transfer Level) into a netlist simple flow diagram.

## Slide 88
From RTL To GDSⅡ design process

## Slide 89: Flowchart front end

## Slide 90: From netlist To GDSⅡ in the design process

## Slide 91: From Schematic To GDSⅡ design process

## Slide 92
Tcl Script{for design vision tool} look like as below
1
2

## Slide 93
3

## Slide 94
Tcl Script{for RTL compiler tool} look like as below
1
2
Encounter Tcl Script we will see at the time of use

## Slide 95: Direct form of FIR filter

## Slide 100: Transpose form of FIR filter

## Slide 104: Bit serial and digit serial design

## Slide 105: Bit serial adder

## Slide 106
Digit serial ( size is 2 ) digit_SA2

## Slide 110
Thank You
Questions
?